## Slide 1
Sulfur hexafluoride (SF6) in the atmosphere today
Steve Montzka, NOAA
Sources of information used in this analysis:
- 2022 Scientific Assessment Panel Report (WMO/UNEP)
- The peer-reviewed scientific literature
(e.g., Simmonds et al., 2020; Hu et al., 2023; Vojta et al., 2024; Western et al., 2025)
- Data from NOAA and AGAGE (publicly available)
Focus of today’s presentation:
- Background information on sources & removals; climate metrics
- Global-scale atmospheric abundance and implied emissions
- contributions to climate warming
- Regional-scale emission contributions
Thanks to colleagues at NOAA and AGAGE, particularly L. Western & X. Lan. September, 2025

## Slide 2
Sulfur hexafluoride (SF6):
* one of the 6 “basket of gases” named in the Kyoto Protocol to the UNFCCC
Sources:
* Industrial production for use in:
- high-voltage electrical equipment as a dielectric and insulator in gas-insulated switchgear, gas circuit breakers, high-voltage lines, and transformers. (80%)
  magnesium industry (4%),
  electronics industry (8%),
  misc. (8%)
* natural sources are insignificant

## Slide 3
Sulfur hexafluoride (SF6):
Removals:
UV photolysis and reactions with electrons in upper atmosphere (mesosphere),
- lifetime (850-1280 years*)
In the absence of emissions, the atmospheric concentration of SF6 would decline at 0.08 to 0.12% yr-1.
Given that the climate influence of a long-lived gas is proportional to its atmospheric concentration, a pulse of SF6 or other long-lived gas will affect Earth’s radiative balance for hundreds of years.
The GWP100 of SF6 is 24700.
The GWP100 metric does not include climate influences >100 years in future
* SAP 2022 Assessment (Burkholder and Hodnebrog, 2022)
Atmospheric decline in the absence of emission
lifetime

## Slide 4
Atmospheric surface measurements of SF6 (2005 - 2021)
Data are predominantly from NOAA and AGAGE
Latitude
Longitude
Black = flask
Red = on-site
From Vojta et al. (2024)

## Slide 5
Parts per trillion (ppt)
SF6 is measured consistently by both NOAA and AGAGE
Concentrations were much lower in the late 1970s compared to today
The rate of increase was about 3.7% yr-1 over the past decade (0.37 ppt yr-1) and is accelerating.
year
Source: NOAA web data and Simmonds et al. (2020)
* pre-1997 AGAGE results are based on measurements at one site (40 S) using an air archive
Global atmospheric surface abundance of SF6
Notes: Doubling time is ~20 years

## Slide 7
SF6 global emission
year
SF6 global emission (Gg yr-1)
Atmosphere-
derived
From Simmonds et al. (2020)
Global emissions have steadily increased since 2000
NOAA
AGAGE
Note 1 Gg = 1 kt

## Slide 8
SF6 global emission
Global emissions have steadily increased since 2000
Atmosphere-derived emissions are substantially larger than UNFCCC augmented reporting totals (gaps filled for some years for non-Annex1 countries)
year
SF6 global emission (Gg yr-1)
Atmosphere-
derived
UNFCCC total
UNFCCC non-Annex1
UNFCCC Annex1
Substantial declines are reported from Annex1 countries; increases from non-Annex1 countries
From Simmonds et al. (2020)
NOAA
AGAGE

## Slide 9
SF6 global emission
Global emissions have steadily increased since 2000
Atmosphere-derived emissions are substantially larger than UNFCCC augmented reporting totals (gaps filled for some years for non-Annex1 countries)
year
SF6 global emission (Gg yr-1)
Atmosphere-
derived
UNFCCC total
UNFCCC non-Annex1
UNFCCC Annex1
A large GAP exists between atmosphere-derived and UNFCCC total emissions
GAP
From Simmonds et al. (2020)
Substantial declines are reported from Annex1 countries; increases from non-Annex1 countries
NOAA
AGAGE

## Slide 10
Emissions of SF6 from the U.S.
U.S. Emission (Gg yr-1)
Atmosphere-
derived
U.S. EPA
Inventory
(submitted to
UNFCCC)
Electric power transmission and distribution
Electrical equipment manufacturing
Magnesium production
Electronics industry
NOAA analysis in Hu et al. (2023)
Atmospheric observations confirm the substantial decline in U.S. inventory emissions over time
Underreporting is apparent, particularly in earlier years
U.S. accounted for 0.39 Gg SF6, or ~4% of global total emissions, in 2018.

## Slide 11
Other regional emissions derived from atmospheric observations
Global network poorly constrains emissions from Africa, India, S. America
Global total –
Atmosphere-
based
inversion
China, global network (53%)
U.S.A., global network (5%)
From Simmonds et al. (2020) and Vojta et al. (2024)
SF6 emissions(Gg yr-1)
China, Gosan measurements only
E.U., global network (3%)
Percentages are contributions to the global total in 2021
China to UNFCCC

## Slide 12
Emissions
(MMt CO2 -eq yr-1)
Comparing the global climate impacts of SF6 to HFC-23 and other gases
Forcing (mW m-2)
Chemical RF (mW m-2) Emiss. (CO2-eq, MMT yr-1)
SF6 5.8 250 +/- 15
HFC-23 6.5 210 +/- 10
CFC-11 70 300 +/- 60
CFC-12 195 308 +/- 260
HCFC-22 52 654 +/- 100
HFC-134a 22 360 +/- 40
CFCs 286 700 +/- 400
HCFCs 61 700 +/- 100
HFCs 46 1220 +/- 50
GWPSF6 = 24700 vs 14700
LifetimeSF6 = 850 - 1280 yr vs 228 yr
R.E.SF6 = 0.574 vs 0.193 Wm-2 ppb-1
Values in ~2020-2023

## Slide 13
Summary, p. 1 of 2
SF6 is an extremely long-lived, human-produced, potent greenhouse gas:
* the impacts of emissions today will be with us for thousands of years
(40% of today’s emission will be in the atmosphere in the year 3000).
* stabilization of atmospheric concentrations is only achievable with near-zero emissions.
The current contribution of SF6 to global radiative heating is:
* comparable to HFC-23
* 15% of all HFCs;
* 1.8% of all Montreal-Protocol controlled gases.
A substantial gap exists in our understanding of global emissions
* Global SF6 emissions are substantially larger than reporting to UNFCCC
* Global SF6 emissions in 2023 were 10.2 +/- 0.6 kt yr-1 (250 MMt CO2-eq yr-1)
and recently are comparable to those of HFC-23, CFC-11, and HFC-134a
* China accounts for about half of recent global emissions
emissions from all continents are not well characterized

## Slide 14
Summary, p. 2 of 2
SF6 emissions continue to increase even in the presence of UNFCCC controls
Mitigation efforts can be effective
* substantial declines are reported for the sum of Annex1 countries
* an emission decline is confirmed by atmospheric data in the U.S.
Without further mitigation efforts large increases in SF6 emissions seem likely
* as society moves away from fossil fuels and electrifies power grids.